## Slide 1
User-training on Uncertainty mode
M. Perez
Innovative Systems Software

## Slide 2: Exercise 1. Simple pipe analysis.

## Slide 3: Exercise 1. Statement
Perform an uncertainty analysis on outlet junction mass flow in the Simple pipe problem. Use the uncertainty information provided in next slides.
Prepare the setup input file spUNC.is from the uncertainty information provided in the exercise.
Run the setup phase of the uncertainty package.
Prepare a batch file to execute automatically all uncertainty runs, from run 0 (base case) to run 59.
Run the simulation phase of the uncertainty package.
Prepare the post-processing input file spUNC.ip to specify the output quantities under analysis.
Run the post-processing phase of the uncertainty package.

## Slide 4: 1. Simple pipe nodalization
110
130
125
120
127

## Slide 5: 1. Setup phase Required information
Card 29000000 – Wilks’ formula data:
First and last uncertainty run numbers
Confidence level and percentile
Order of application
Number of added runs (optional field)
Minimum and maximum number of runs (optional field)
Seed (optional field)
Cards 29100XXXX – Source correlation parameters, uncertainty information.
Cards 291DDWWW – Input treatable parameters, uncertainty information.

## Slide 6: 1. Setup phase Input treatable parameters
Associate uncertainty to the following input treatable parameters:
Pressure in source tmdpvols
Uniform Distribution: min. = 0.97, max. = 1.03
Temperature in source tmdpvols’
Normal Distribution: mean = 1.0, standard deviation = 0.03
Valve control system: Setpoint mass flow
  Uniform Distribution: min. = 0.98, max. = 1.02
  Valve control system: Integral-constant
  Uniform Distribution: min. = 0.95, max. = 1.05
Stainless steal material properties: Thermal conductivity
  Trapezoidal Distribution: [0.95,0.97,1.02,1.05]
  Stainless steal material properties: Heat capacity
  Trapezoidal Distribution: [0.98,1.0,1.01,1.02]

## Slide 7: 1. Setup phase Source correlation parameters
Associate uncertainty to the following code correlations’ coefficients:
Interphase heat transfer to liquid in bubbly flow regime: HTC.02.101
Uniform Distribution: min. = 0.8, max. = 1.2
Single phase liquid wall to liquid heat transfer: FRV.BBY.HIF
Uniform Distribution: min. = 0.8, max. = 1.2
Liquid viscosity: VIS.LW.LIZ
Normal Distribution: mean = 1.0, standard deviation = 0.02
Liquid conductivity: CON.LW.LIQ
Normal Distribution: mean = 1.0, standard deviation = 0.02
Liquid surface tension: SFT.LW.LV
Normal Distribution: mean = 1.0, standard deviation = 0.02

## Slide 8: 1. Setup phase Examples
Pressure in source tmdpvol CCC=110
Uniform Distribution: min. = 0.97, max. = 1.03
Interphase heat transfer to liquid in bubbly flow regime: HTC.02.101
Uniform Distribution: min. = 0.8, max. = 1.2
Card 291DDWWW | W1 | W2 | W3 | W4 | W5 | W6
29101000 | UD | 0.97 | 1.03 | 0.0 | 0.0 | 
29101001 | -1.0 | 20 | 1100201 | 2 | 2 | 1
29101002 | -1.0 | … |  |  |  | 
Card 2900NNNN | W1 | W2 | W3 | W4 | W5 | W6 | W7 | W8
29000001 | HTC.02.101 | UD | 0.80 | 1.20 | 0.0 | 0.0 | -1.0 | 0.0
29000002 |  |  |  |  |  |  |  | 

## Slide 9: 1. Simulation phase Batch file
Prepare a batch file to automatically execute all uncertain code runs
Example:
relap5.exe –i spUNC.i –uncrun 0 –Q
relap5.exe –i spUNC.i –uncrun 1 –Q
relap5.exe –i spUNC.i –uncrun 2 –Q
…
Notes:
Number “0” refers to base case, i.e. no uncertainty weights are applied
Field “–Q” exits the calculation automatically

## Slide 10: 1. Post-processing phase Input file
To obtain the uncertainty bands specify the uncertain code runs to be used and the desired output variables.
Example:
292000000 1 -59 uses runs number 1 to number 59
208090001 mflowj 127000000 indicates mass flow through valve 127

## Slide 11: Exercise 2. Simple plant analysis.

## Slide 12: Exercise 2. statement
Perform an uncertainty analysis on the maximum cladding temperature in the Simple plant problem simulating a station blackout. Use the uncertainty information provided in next slides.
Merge the steady-state and transient files into a single input file.
Prepare the setup input file splantUNC.is from the uncertainty information provided in the exercise.
Run the setup phase of the uncertainty package.
Prepare a batch file to execute automatically all uncertainty runs, from run 0 (base case) to run 59.
Run the simulation phase of the uncertainty package.
Prepare the post-processing input file splantUNC.ip to specify the output quantities under analysis.
Run the post-processing phase of the uncertainty package.

## Slide 13: 2. Previous step Merge the steady-state and transient files
Merge the steady-state and transient files into a single file and make the appropriate modifications to obtain the same results. Check the behavior of:
Steady-state controllers
  “pumpctl”
  “steamctl”
  “feedctl”
Pressurizer re-nodalization and associated logic
Transient
  cards 100, 201
  Power scram curve trip
In addition, add maximum cladding temperature card in fuel HSs.

## Slide 14: 2. Setup phase Input treatable parameters
Associate uncertainty to the following input treatable parameters:
Steady-state primary mass flow (pump velocity controller “pumpctl”)
Normal Distribution: mean = 1.0, standard deviation = 0.025
Steady-state secondary pressure (valve area controller “steamctl”)
Normal Distribution: mean = 1.0, standard deviation = 0.01
Steady-state primary pressure
  Normal Distribution: mean = 1.0, standard deviation = 0.01
  Initial gap internal pressure (gap conductance model)
  Normal Distribution: mean = 1.0, standard deviation = 0.05
Initial core power
  Normal Distribution: mean = 1.0, standard deviation = 0.01
  Power scram curve
  Normal Distribution: mean = 1.0, standard deviation = 0.01

## Slide 15: 2. Setup phase Input treatable parameters, cont’d
Axial core power.
Change the axial core power by associating a multiplier to central core nodes (node 06 and 07): the multiplier ranges from 1.0 (‘flat’ profile) to greater values.
Use the normalization capability in all active core nodes to keep the sum of all axial core power multipliers equal to one.
Uniform Distribution: min. = 1.0, max. = 1.2
Reactor scram occurrence (modification of timeof in trip T-506)
Convert the uncertainty given in seconds into a multiplier.
Uniform Distribution: min. = 3.0 sec., max. = 7 sec.

## Slide 16: 2. Setup phase Source correlation parameters
Associate uncertainty to the following code correlations’ coefficients:
Gap conductivity (gap conductance model)
Uniform Distribution: min. = 0.9, max. = 1.1
Wall-to-fluid heat transfer.
Table 4.2-1 Wall Convection Heat Transfer Numbers in R5 manual volume IV.
  Single-phase liquid. Uniform Distribution: min. = 0.9, max. = 1.1
  Subcooled nucleate boiling. Uniform Distribution: min. = 0.9, max. = 1.1
  Saturated nucleate boiling. Trapezoidal Distribution [0.88, 0.95, 1.1, 1.13]
  Subcooled transition boiling. Trapezoidal Distribution [0.9, 0.95, 1.05, 1.1]
  Subcooled film boiling. Trapezoidal Distribution [0.9, 0.95, 1.05, 1.1]
  Saturated film boiling. Trapezoidal Distribution [0.9, 0.95, 1.05, 1.1]
  Filmwise condensation. Uniform Distribution: min. = 0.9, max. = 1.1

## Slide 17: 2. Setup phase: Uncertainty information Source correlation parameters, cont’d
Interphase heat transfer. Apply uncertainty coefficients to liquid side.
Uniform Distribution: min. = 0.93, max. = 1.07
  Bubbly flow regime.
  Annular flow regime.
  Slug flow regime.
  Mist pre-CHF flow regime.

## Slide 18: 2. Simulation phase Batch file
Prepare a batch file to automatically execute all uncertain code runs
Example: batch file splantUNC.bat
relap5.exe –i splantUNC.i –uncrun 0 –Q
relap5.exe –i splantUNC.i –uncrun 1 –Q
relap5.exe –i splantUNC.i –uncrun 2 –Q
…

## Slide 19: 2. Post-processing phase Input file
To obtain the uncertainty bands specify the uncertain code runs to be used and the desired output variables.
Example:
292000000 1 -59 uses runs number 1 to number 59
20809001 httemp 110001010
20809002 mflowj 201000000
20809003 mflowj 231000000
20809004 httemp 110000810
20809006 p 140010000
20809006 p 160010000
20809007 p 230010000
20809008 pmpvel 170
20809009 tempf 140010000
20809010 tempf 160010000

## Slide 20: Exercise 3. SBLOCA analysis.

## Slide 21: Exercise 3. statement
Perform an uncertainty analysis on maximum cladding temperature, break mass flow and primary side pressure in a SBLOCA scenario. Use the uncertainty information provided in next slides.
Prepare the input file from typpwrUNC.i.
Prepare the setup input file typpwrUNC.is from the uncertainty information provided in the exercise.
Run the setup phase of the uncertainty package.
Prepare a batch file to execute all uncertainty runs.
Run the simulation phase of the uncertainty package.
Prepare the post-processing input file typpwrUNC.ip to specify the output quantities under analysis.
Run the post-processing phase of the uncertainty package.

## Slide 22: 3. Setup phase Wilks’ formula
Use Wilks’ formula at 3rd order to obtain the 5/95 and 95/95 unilateral tolerance limits:
The 5/95 unilateral tolerance limit defines the region that contains the 5% of the population (5th percentile) under study with a confidence level of 0.95
The 95/95 unilateral tolerance limit defines the region that contains the 95% of the population (95th percentile) under study with a confidence level of 0.95
The 3rd order of application requires 124 calculations to determine the uncertainty limits:
    5/95 = rank(3)
    95/95 = rank(122)
    Find the information on the number of calculations, percentile and confidence level given in the output-print file typpwrUNC.os.

## Slide 23: 3. Setup phase Input treatable parameters
Associate uncertainty to the following input treatable parameters:
Axial peaking factor in core node 03 (maximum). Introduce normalization option to all nodes to keep the overall sum of the axial peaking factors to 1.0.
Normal Distribution: mean = 1.0, standard deviation = 0.025
Initial total reactor power.
Normal Distribution: mean = 1.0, , standard deviation = 0.010
Fuel volumetric heat capacity. Temperature range:
  T≤2732K. Normal Distribution: mean = 1.0, , standard deviation = 0.010
  T>2732. Normal Distribution: mean = 1.0, , standard deviation = 0.066
Fuel thermal conductivity. Temperature range:
  T≤3100K. Normal Distribution: mean = 1.0, , standard deviation = 0.051
  T>3100K. Normal Distribution: mean = 1.0, , standard deviation = 0.102
Fission product yield factor.
Normal Distribution: mean = 1.0, , standard deviation = 1.2

## Slide 24: 3. Setup phase Input treatable parameters, cont’d
Scram curve at time ≥ 0.9 seconds. Use option to limit the product of the base value and the weight to 1.0.
Normal Distribution: mean = 1.0, standard deviation = 0.01
Break size*.
Uniform Distribution: min. = 0.9 , max. = 1.1
Choked flow model at the break for subcooled and 2-phase flow conditions. Use one multiplier per parameter.
Uniform Distribution: min. = 0.8, max. = 1.2
SI delay*.
Uniform Distribution: min. = 3 seconds, max. = 8 seconds
Charging delay*.
Uniform Distribution: min. = 3 seconds, max. = 8 seconds
Auxiliar feed flow delay.
Uniform Distribution: min. = 10 seconds, max. = 20 seconds

## Slide 25: 3. Setup phase Input treatable parameters, cont’d
Comments to input treatable parameters:
Symbol * indicates that the implementation of the parameter’s uncertainty requires input file modification.
Notice that not all the uncertainty information is provided in a multiplier form. Convert the non-multipliers to multipliers (the uncertainty package requires the information in a multiplier form).
Notice that, since the input typpwrUNC.i does not simulate a steady-state period, the plant initial conditions cannot be included in the uncertainty analysis.

## Slide 26: 3. Setup phase Source correlation parameters
Associate uncertainty to the following code correlations’ coefficients:
Wall-to-fluid heat transfer. Apply uncertainty to “default” and “bundle without cross-flow” * convective boundary conditions (different convective boundary conditions but same distribution information).
  Single-phase liquid. Uniform Distribution: min. = 0.8, max. = 1.2
  Subcooled nucleate boiling. Uniform Distribution: min. = 0.35, max. = 2.5
  Saturated nucleate boiling. Trapezoidal Distribution [0.78, 0.85, 1.2, 1.4]
  Subcooled transition boiling. Trapezoidal Distribution [0.8, 0.85, 1.2, 1.3]
  Saturated transition boiling. Trapezoidal Distribution [0.8, 0.85, 1.2, 1.3]
  Single-phase vapor. Uniform Distribution: min. = 0.8, max. = 1.2
  Light water, liquid viscosity.
  Normal Distribution: mean = 1.00, standard deviation = 0.02

## Slide 27: 3. Setup phase Source correlation parameters, cont’d
Light water, liquid conductivity.
Normal Distribution: mean = 1.00, standard deviation = 0.02
  Light water, surface tension.
  Normal Distribution: mean = 1.00, standard deviation = 0.02
  Critical heat flux*. Groeneveld lookup table method.
  Uniform Distribution: min. = 0.90, max. = 1.10
  Gap conductivity using gap conductance model*.
  Uniform Distribution: min. = 0.80, max. = 1.20
Interphase heat transfer. Apply uncertainty coefficients to liquid side.
Uniform Distribution: min. = 0.93, max. = 1.07
  Bubbly flow regime.
  Annular flow regime.
  Slug flow regime.
  Mist pre-CHF flow regime.
  Mist post-dryout flow regime.

## Slide 28: 3. Setup phase Source correlation parameters, cont’d
Comments to source correlation parameters:
Symbol * indicates that the implementation of the parameter’s uncertainty requires input file modification:
Bundle convective condition for fuel and steam generators’ (primary side) heat structures (use P/D = 1.25)
Gap conductance model (use initial gap internal pressure = 349.54 lbf/in2). Note: only 1 mesh interval is allowed when using gap conductance model.
Maximum cladding temperature in fuel heat structures
Notice that not all the uncertainty information is provided in a multiplier form. Convert the non-multipliers to multipliers (the uncertainty package requires the information in a multiplier form).
Notice that, since the input typpwr.i does not simulate a steady-state period, the plant initial conditions cannot be included in the uncertainty analysis.

## Slide 29: 3. Simulation phase Batch file
Prepare a batch file to execute the base case (run number 0) and the uncertainty runs (run numbers 1 to 124).
Add the “-Q “ field at the end of each command line so that the code quits the Relap execution window automatically after each calculation.
Note the numbers attached to each output-print and restart-plot files.

## Slide 30: 3. Post-processing phase Input file
Prepare the post-processing input file to request the data for the following output quantities:
  Maximum cladding temperature
  Break mass flow
  Primary pressure